Low Cost H-Line Receiver Software Tools

For MS Windows/DOS – 32bit, (64bit) and Linux versions in [] brackets.

| Program | Function | Command Line (Win32) |
| --- | --- | --- |
| AMP_STS.EXE(2) (amp_sts64.exe(3)) [amp_stats(4)] | Takes rtl_sdr.exe(1) binary file and outputs a text file of the SDR ADC data distribution. | AMP_STS <infile> <outfile> |
| BIN_TXT.EXE(5) (bin_txt64.exe(6) ) [bin_txt(7)] | Takes rtl_sdr.exe(1) binary file and outputs a text file of the SDR ADC data. | BIN_TXT <infile> <outfile> <number of 8192 sample data blocks> |
| RAFFT.EXE(8) (r64fft.exe(9) ) [rafft(10)] | Takes rtl_sdr.exe(1) binary file applies the FFT algorithm to data blocks, and averages these over the input data length and outputs a text file | RAFFT <infile> <outfile> <Number of FFT points> |
| RAFFT2.EXE(11) r64fft2.exe(12) ) [rafft2(13)] | As above but data offset to reduce the zero frequency spike. | RAFFT2 <infile> <outfile> <Number of FFT points> |
| RN_PRGAT.EXE(14) (r64_prg_at.exe(15) ) [run_prg_at(16)] | Uses PC clock to run any program at a set time, on one or more PCs simultaneously. | RN_PRGAT <”prog.exe”><hr min sec> |
| RUN_RTL.EXE(17) (r64_rtl.exe(18) ) [run_rtl(19)] | Runs the rtl_sdr(1) program and generates a bin file which is then processed with the FFT algorithm to output spectrum averaged text file. | RUN_RTL <”rtl_sdr data.bin + command line”>< Number of FFT points> |
| RN_RTLAT.EXE(20) (r64_rtl_at.exe(21) ) [run_rtl_at(22)] | Uses PC clock to run the rtl_sdr(1) program at a set time, generates a bin file which is then processed with the FFT algorithm to output spectrum averaged text file. | RN_RTLAT <”rtl_sdr data.bin + command line”>< Number of FFT points><hr min sec> |

Reference 23 links to a Zipfile containing all the Low-cost H-Line receiver software tools.

# Running the MS Windows 32 Tools

# Example 1:

- Copy 'command.com' from ‘Windows/system32’ directory, RAFFT2.exe from the link – Reference (16) and your Osmocom ‘rtl_sdr’(1) recorded .bin files to your working directory.

- Open 'command.com', change the directory to your working directory if required and type in:-

RAFFT2 <infile> <outfile> 256

where, 'infile' is your recorded .bin file 'outfile' is any name you choose and could end in .txt as it is a text file. The final command line entry '256' is the number of FFT points you choose. This must be a power of 2.

- Open it in 'notepad', 'select all', 'copy' and 'paste' in 'Excel' and follow Excel instructions to produce a graphic display.

# Example 2

In this example, two SDRs are initiated simultaneously to record digitised data for a set time.

To achieve simultaneous recording, two terminal windows, one for each SDR, run a copy of the control software that is set with the desired recording parameters.

Typical control software commands to run two SDRs (-d 0 and -d 1) on a single computer for MS WINDOWS are,

Command Terminal 1>

RN_RTLAT “./rtl_sdr dat0.bin –f 1420e6 –d 0 –g 49 –n 100e6” 256 14 24 00

Command Terminal 2>

RN_RTLAT “./rtl_sdr dat1.bin –f 1420e6 –d 1 –g 49 –n 100e6” 256 14 24 00

These are run in two Command windows set to the working directory, which also contains the Osmocom rtl_sdr tools.

These commands start recording data from both SDRs at 14hr 24m 0s using the Osmocom rtl_sdr program. In this example, on collection of 100 million samples, the data is analysed in 256 point blocks using a FFT algorithm and outputs averaged spectrum text files dat0.txt and dat1.txt.

Inputting these data text files into Excel or mathcad software the temperature graphs can be produced indicating H-Line characteristics.

## References

- http://sdr.osmocom.org/trac/wiki/rtl-sdr

- http://www.y1pwe.co.uk/RAProgs/dos/AMP_STS.EXE

- http://www.y1pwe.co.uk/RAProgs/linux/amp_sts64.exe

- http://www.y1pwe.co.uk/RAProgs/linux/amp_stats

- http://www.y1pwe.co.uk/RAProgs/dos/BIN_TXT.EXE

- http://www.y1pwe.co.uk/RAProgs/linux/bin_txt64.exe

- http://www.y1pwe.co.uk/RAProgs/linux/bin_txt

- http://www.y1pwe.co.uk/RAProgs/dos/RAFFT.EXE

- http://www.y1pwe.co.uk/RAProgs/linux/r64fft.exe

- http://www.y1pwe.co.uk/RAProgs/linux/rafft

- http://www.y1pwe.co.uk/RAProgs/dos/RAFFT2.EXE

- http://www.y1pwe.co.uk/RAProgs/linux/r64fft2.exe

- http://www.y1pwe.co.uk/RAProgs/linux/rafft2

- http://www.y1pwe.co.uk/RAProgs/dos/RN_PRGAT.EXE

- http://www.y1pwe.co.uk/RAProgs/linux/r64_prg_at.exe

- http://www.y1pwe.co.uk/RAProgs/linux/run_prg_at

- http://www.y1pwe.co.uk/RAProgs/dos/RUN_RTL.EXE

- http://www.y1pwe.co.uk/RAProgs/linux/r64_rtl.exe

- http://www.y1pwe.co.uk/RAProgs/linux/run_rtl

- http://www.y1pwe.co.uk/RAProgs/dos/RN_RTLAT.EXE

- http://www.y1pwe.co.uk/RAProgs/linux/r64_rtl_at.exe

- http://www.y1pwe.co.uk/RAProgs/linux/run_rtl_at

- http://www.y1pwe.co.uk/RAProgs/LCHlineSW.zip

PW East October 2014