RFI Interference and Pulsar Detection

Peter W East

Introduction

This note follows on from  the paper Amateur Pulsar Detection1 and investigates the effects of RF interference on pulsar detection SNR. Whilst the synchronous integration/folding technique (rapulsar.exe) is an excellent period tuning discriminator for noise and interference suppression when recovering the pulsar pulse, RF interference (RFI), if close in frequency to the pulsar period can seriously impair the period matching process, especially for weak pulsar signals.

An investigation into RFI mitigation using a 1 GB Vela pulsar data file supplied by GM Gancio2 has shown that a useful improvement in SNR is obtained by narrow-band harmonic filtering the RFI before applying the folding algorithm. Considering the example in Figure 1 but now using 98 bins, the SNR change was from 61 with no filtering to 69 with some RFI filtering. However, the process did offer albeit a small improvement in  pulsar pulse visibility, and so is described.

Figure 1 Vela folded pulse (blue) and main interference component (magenta)

Also plotted in Figure 1 is one cycle of the main RFI component (magenta; interference period 6.27ms) - this was recovered by using the folding technique, primed now with the interference period rather than the pulsar period. In this case, the pulsar signal is suppressed as are other RFI components.

Examining RFI

RFI spectral components were identified by applying and FFT to the data after first downsampling it from 2MHz to 1kHz, using pdetect software1 using the command line,

pdetect 500.bin pdet500.txt 2.0 1.0 1

The first 131072 samples in this data file were then spectrum analysed in a 131072-point Real FFT in MathCad and the result is plotted in Figure 2.

In this strong signal data, the pulsar spectral lines and RFI components are clearly seen. The pulsar line harmonics, at FFT binn are related to the pulsar period and FFT properties from,

where, Q = number of FFT points, T = the pulsar period and Bv the downsizing video bandwidth (1kHz)

Figure 2 Data File 500.bin Real Spectrum (red).

Blue Plot:- manually reduced RFI by 20dB

In this example (Figure 2),  bin numbers expected to contain pulsar modulation harmonics, are 0, and Int[n.1466.286], where n = 1,2,3 ....etc:, and Int[]  represents the integer part. Bins containing the larger RFI components are easily identified and attenuated or removed by manually adjusting a set of digital bin-blocking filters.

Figure 3 Data Plots, blue: raw data; red: RFI filtered data; black: pulsar pulses

From Figure 3, it is clear in the RFI filtered data (red) that the larger pulsar pulses are much more visible and there is some pulsar amplitude scintillation evident. The red filtered time plot was obtained by taking the inverse FFT of the filtered spectrum data.

In the third (black) plot many more lower level pulsar pulses can be identified and the process to obtain this will now be explained.

Extracting Individual Pulsar Pulses

By setting up a narrow-band harmonic repeating filter gate about the pulsar spectral lines and then taking the inverse FFT of this data, the pulsar pulse train modulation at the pulsar period can be extracted and plotted as shown in the red plot of Figure 4.

Figure 4 Data Plots, red: pulsar modulation; black: pulsar pulses

In fact, this data exhibits the pulsar pulse modulation shape and phase but without the individual pulse amplitudes. The amplitude data, however can be recovered by using this pulse train to control a harmonic time gate, selecting the pulsar pulses from the filtered time data giving rise to the black plot of pulsar pulses; now including amplitude and pulse shape. Detail is shown in Figure 5. Note small individual pulses can still be corrupted system residual RFI and noise.

Figure 5 Pulsar Pulse Modulation Detail

Conclusions

This document has described the processes required to identify and remove the  main RFI components from the data spectrum.

On strong signals and where the RFI harmonics do not clash with the pulsar spectral components, a useful improvement in SNR is possible. However, with weak signals, although pulsar period and spectral components may be known, RFI filtering may not always be effective.

Extracting pulsar modulation properties by filtering, inverse transforming and then time gating gives useful information on amplitude scintillation of strong pulsars. The filtered data can then be folded to produce and improved SNR.

PW East July 2015

# Footnotes

1 Amateur Pulsar Detection. PW East & GM Gancio.  BAA RAGazine Vol 3, Issue 1, Aug. 2015. http://www.britastro.org/radio/ragazine/RAGazine_2015_Aug.pdf

http://www.y1pwe.co.uk/RAProgs/AmateurPulsarDetectionF.doc

2 Institute of Radio Astronomy, Argentina.